## Slide 1
HCRecov — Monomer Recovery Assessment
Nitrogen Purge Stream | PP Plant | Hazira Manufacturing Division
Reliance Industries Ltd., Hazira Manufacturing Division
Summer Internship — Batch 2026 · June 2026
Project: HCRecov · Run 2
Reliance Industries Ltd., Hazira Manufacturing Division · Summer Internship — Batch 2026 · Slide 1 / 10

## Slide 2
Scope & Feed Conditions | HCRecov Assessment
June 2026
Reliance Industries Ltd., Hazira Manufacturing Division · Summer Internship — Batch 2026 · Slide 2 / 10
Process Scope & Boundary Conditions
Assessment Scope
First-principles assessment of three hydrocarbon recovery technologies for a 650 kg/hr purge stream at 1.20 bar(a) and 64 °C (5 mol% C3H6).
650 kg/hr
Feed Flow
1.20 bar(a)
Pressure
64 °C
Temperature
5 mol%
HC (C3H6)
Technologies Assessed
① Hollow-Fiber Polymeric Membrane Skid
② Twin-Bed Pressure Swing Adsorption (PSA)
③ Heavy Hydrocarbon Gas Absorption Loop

## Slide 3
Recovery Efficiency Comparison
June 2026
Reliance Industries Ltd., Hazira Manufacturing Division · Summer Internship — Batch 2026 · Slide 3 / 10
Net Monomer Recovery Efficiency by Technology
Feed: 1.20 bar(a) · 64 °C · 5 mol% C3H6 · Target ≥ 90%
Chart: 
| Membrane | PSA (Adsorption) | Absorption
Recovery Efficiency (%) | 95.8 | 98.5 | 98
Min. Target 90%

## Slide 4
Capital Expenditure (CAPEX) Comparison
June 2026
Reliance Industries Ltd., Hazira Manufacturing Division · Summer Internship — Batch 2026 · Slide 4 / 10
Package Installed CAPEX by Technology
Standard Catalog Equipment · 2026 Cost Index (USD × 1 000)
Chart: 
| Membrane | PSA (Adsorption) | Absorption
CAPEX (× $1000) | 778 | 73 | 105
Note: Membrane CAPEX includes K-301 feed gas booster
compressor (1.2 → 16.2 bar)

## Slide 5
Hollow-Fiber Polymeric Membrane Skid System
June 2026
Reliance Industries Ltd., Hazira Manufacturing Division · Summer Internship — Batch 2026 · Slide 5 / 10
Membrane Skid — Component Breakdown
Component | Rating | Max Capacity | Used Capacity | CAPEX | OPEX/hr
K-301 Feed Gas Booster Compressor | API 619 Screw Machine / 110.0 kW Motor Enclosure | 126.5 kW thermal limit | 94.6 kW compression work | $172,000 | $8.80
M-301 Polyimide Membrane Separator Skids | ASME Rated Bank housing 14 Standard Elements | 560.0 m2 active area barrier | 537.6 m2 selective flux interface (log-mean ΔP = 0.241 bar) | $605,700 | $25.49
TOTAL |  |  |  | $777,700 | $34.29
Net Recovery Efficiency: 95.8% · Total Package CAPEX: $777,700 · Total OPEX: $34.29/hr
K-301: Isentropic Pressure Ratio: 13.5:1 | p_discharge = 16.2 bar (from process_parameters.json)
M-301: Calculated Permeate Matrix Gas Recovery: 95.8% | OPEX breakdown: replacement + auxiliaries = $25.49/hr

## Slide 6
Twin-Bed Cyclic Pressure Swing Adsorption Skid
June 2026
Reliance Industries Ltd., Hazira Manufacturing Division · Summer Internship — Batch 2026 · Slide 6 / 10
PSA Skid — Component Breakdown
Component | Rating | Max Capacity | Used Capacity | CAPEX | OPEX/hr
Y-201 Duplex Guard Cartridge Element | ASME Housing / 0.5 Micron Particulate Strainer | 740.3 m3/hr hydraulic ceiling | 528.8 m3/hr actual volumetric flow | $18,500 | $0.45
V-201 A/B Twin Swing Adsorber Steel Shells | ASME Section VIII / ANSI 150# Rating Vessel Frame | 230.7 kg standard loading frame | 142.6 kg required sieve mass | $54,400 | $3.50
TOTAL |  |  |  | $72,900 | $3.95
Net Recovery Efficiency: 98.5% · Total Package CAPEX: $72,900 · Total OPEX: $3.95/hr
Y-201: 99.95% Resin Fines Separation Guard
V-201: Langmuir Pore Vapor Equilibrium Affinity: 98.5% | Cycle: 10 min total / feed step 40% (4.0 min)

## Slide 7
Heavy Hydrocarbon Gas Absorption Recirculation Loop
June 2026
Reliance Industries Ltd., Hazira Manufacturing Division · Summer Internship — Batch 2026 · Slide 7 / 10
Absorption Loop — Component Breakdown
Component | Rating | Max Capacity | Used Capacity | CAPEX | OPEX/hr
E-101 Feed Gas Cooler (Shell & Tube) | TEMA R / ANSI 150# — CW Duty Gas Cooler | 15.2 m2 surface (25% margin envelope) | 12.2 m2 required transfer surface ¦ Duty: 5.7 kW | $19,200 | $0.00
T-101 Absorber Tower Packed Shell | ASME Section VIII / ANSI 150# Low Press Casing | 1142.2 kg/hr hydraulic ceiling | 650.0 kg/hr @ 35 °C (post E-101) | $76,800 | $9.57
P-101 A/B Solvent Circulation Pumps | API 610 Centrifugal / Standard 7.5 kW Frame | 12.0 GPM impeller cut | 9.6 GPM solvent circulation | $9,400 | $8.92
TOTAL |  |  |  | $105,400 | $18.49
Net Recovery Efficiency: 98.0% · Total Package CAPEX: $105,400 · Total OPEX: $18.49/hr
E-101: Cooling duty: 64.0 °C → 35.0 °C | d-T_lm = 10.5 K | NOTE: E-101 is a missing upstream unit — without it the absorber operates at feed temperature (64 °C), raising Henry's constant and requiring ~65× L/G to compensate.
T-101: Thermodynamic Recovery Yield: 98.0% | Absorption Factor A = 1.50 | L/G (mass) = 2.7 | C_design = 0.0770 m/s (Mellapak 250Y @ 72% flood)
P-101: Solvent Recirculation Loop Containment

## Slide 8
Technology Comparison Matrix
June 2026
Reliance Industries Ltd., Hazira Manufacturing Division · Summer Internship — Batch 2026 · Slide 8 / 10
Multi-Criteria Technology Comparison
Criterion | Membrane | PSA | Absorption
Recovery Efficiency (%) | 95.8% | 98.5% | 98.0%
CAPEX (USD k) | $777.7k | $72.9k | $105.4k
Meets 90% Target | Yes | Yes | Yes
Operability | High | Medium | High
Maintenance | Low | Medium | Medium
Footprint | Medium | Large | Large
Recommended | ✓ YES | ✓ YES | ✓ YES

## Slide 9
Key Findings & Engineering Recommendation
June 2026
Reliance Industries Ltd., Hazira Manufacturing Division · Summer Internship — Batch 2026 · Slide 9 / 10
Key Findings
1
Polymeric Membrane achieves 95.8% recovery — meets target; CAPEX $777.7k.
2
Pressure Swing Adsorption achieves 98.5% recovery — meets target; CAPEX $72.9k.
3
Heavy Gas Absorption achieves 98.0% recovery — meets target; CAPEX $105.4k.
RECOMMENDATION · Pressure Swing Adsorption is the primary recommendation, meeting the recovery target at the lowest CAPEX ($72.9k). Polymeric Membrane, Heavy Gas Absorption also meet the target and remain viable alternatives.

## Slide 10
Summary
Feed: 650 kg/hr · 1.2 bar(a) · 64 °C · 5 mol% C3H6
Membrane: 95.8% recovery | CAPEX $777.7k · Meets target
PSA: 98.5% recovery | CAPEX $72.9k · Meets target
Absorption: 98.0% recovery | CAPEX $105.4k · Meets target
Primary Recommendation: Pressure Swing Adsorption (lowest CAPEX among options meeting target)
Generated: 2026-06-30T02:44:13 · HCRecov Run 2