## Slide 1
HCRecov Industrial Sizing Ledger
Purge Stream Analysis — Basis: 650.0 kg/hr
HCRecov Demonstration Plant
HCRecov Engineering Team · June 2026
Project: HCRecov · 1.0
HCRecov Demonstration Plant · HCRecov Engineering Team · Slide 1 / 10

## Slide 2
Scope & Feed Conditions | HCRecov Assessment
June 2026
HCRecov Demonstration Plant · HCRecov Engineering Team · Slide 2 / 10
Process Scope & Boundary Conditions
Assessment Scope
Industrial Unit-Level First-Principles Assessment
650 kg/hr
Feed Flow
1.20 bar(a)
Pressure
64 °C
Temperature
5 mol%
HC (C3H6)
Technologies Assessed
① Hollow-Fiber Polymeric Membrane Skid
② Twin-Bed Pressure Swing Adsorption (PSA)
③ Heavy Hydrocarbon Gas Absorption Loop

## Slide 3
Recovery Efficiency Comparison
June 2026
HCRecov Demonstration Plant · HCRecov Engineering Team · Slide 3 / 10
Net Monomer Recovery Efficiency by Technology
Feed: 1.20 bar(a) · 64 °C · 5 mol% C3H6 · Target ≥ 90%
Chart: 
| Membrane | PSA (Adsorption) | Absorption
Recovery Efficiency (%) | 78.5 | 76.2 | 72.8
Min. Target 90%

## Slide 4
Capital Expenditure (CAPEX) Comparison
June 2026
HCRecov Demonstration Plant · HCRecov Engineering Team · Slide 4 / 10
Package Installed CAPEX by Technology
Standard Catalog Equipment · 2026 Cost Index (INR × 1 000)
Chart: 
| Membrane | PSA (Adsorption) | Absorption
CAPEX (× ₹1000) | 137775 | 118570 | 93520
Note: Membrane CAPEX includes K-301 feed gas booster
compressor (1.2 → 16.2 bar)

## Slide 5
Polymeric Membrane Separation
June 2026
HCRecov Demonstration Plant · HCRecov Engineering Team · Slide 5 / 10
Membrane Skid — Component Breakdown
Component | Rating | Max Capacity | Used Capacity | Flow Rate | ΔP | CAPEX | OPEX/hr
Feed Suction Knock-Out Drum | ASME Sec VIII Div 1, Vert Shell (600mm x 2.0m) | 740.3 Am3/hr limit | 528.8 Am3/hr | 650.0 kg/hr | 0.02 bar | ₹4,62,000 | ₹6.47
Feed Gas Booster Compressor | API 619 Oil-Injected Screw Process Package | 110.0 kW Motor limit | 67.4 kW Shaft Work | 650.0 kg/hr | -15.0 bar (Pressurize) | ₹5,94,000 | ₹7.96
Coalescing Pre-Filter Element | 0.5 Micron High-Pressure Particulate Shell | 60.7 Am3/hr limit | 39.2 Am3/hr | 650.0 kg/hr | 0.15 bar | ₹7,26,000 | ₹9.44
Polyimide Membrane Separator Skids | ASME Multi-Tube Module Housing (14 Elements) | 560.0 m2 Bank Barrier Matrix | 537.6 m2 Active Area | Retentate: 604.4 kg/hr Permeate: 45.6 kg/hr | 15.00 bar (Trans-membrane) | ₹8,58,000 | ₹10.91
TOTAL |  |  |  |  |  | ₹16,50,000 | ₹18.50
Net Recovery Efficiency: 78.5% · Total Package CAPEX: ₹16,50,000 · Total OPEX: ₹18.50/hr
Feed: Estimated recovery contribution 78.5% with Feed Suction Knock-Out Drum sized for the stated duty.
Feed: Estimated recovery contribution 78.5% with Feed Gas Booster Compressor sized for the stated duty.
Coalescing: Estimated recovery contribution 78.5% with Coalescing Pre-Filter Element sized for the stated duty.
Polyimide: Estimated recovery contribution 78.5% with Polyimide Membrane Separator Skids sized for the stated duty.

## Slide 6
Pressure-Swing Adsorption
June 2026
HCRecov Demonstration Plant · HCRecov Engineering Team · Slide 6 / 10
PSA Skid — Component Breakdown
Component | Rating | Max Capacity | Used Capacity | Flow Rate | ΔP | CAPEX | OPEX/hr
Duplex Guard Particulate Strainer | ASME Y-Pattern Stainless Mesh Core Housing | 740.3 Am3/hr structural limit | 528.8 Am3/hr | 650.0 kg/hr | 0.08 bar | ₹3,97,600 | ₹5.88
PSA Cycle Feed Gas Compressor* | API 619 Heavy Duty Double-Helix Screw Machine | 160.0 kW Motor Enclosure | 84.2 kW Gas Energy | 650.0 kg/hr | -23.8 bar (Pressurize) | ₹5,11,200 | ₹7.22
Twin Adsorber Beds (Interlocked) | ASME VIII Carbon Sieve / Zeolite Dual Bed System | 230.7 kg Vessel Volume | 142.6 kg Sieve Loaded | 650.0 kg/hr cyclical dynamic | 0.12 bar | ₹6,24,800 | ₹8.57
TOTAL |  |  |  |  |  | ₹14,20,000 | ₹16.80
Net Recovery Efficiency: 76.2% · Total Package CAPEX: ₹14,20,000 · Total OPEX: ₹16.80/hr
Duplex: Estimated recovery contribution 76.2% with Duplex Guard Particulate Strainer sized for the stated duty.
PSA: Estimated recovery contribution 76.2% with PSA Cycle Feed Gas Compressor* sized for the stated duty.
Twin: Estimated recovery contribution 76.2% with Twin Adsorber Beds (Interlocked) sized for the stated duty.

## Slide 7
Heavy-Gas Absorption
June 2026
HCRecov Demonstration Plant · HCRecov Engineering Team · Slide 7 / 10
Absorption Loop — Component Breakdown
Component | Rating | Max Capacity | Used Capacity | Flow Rate | ΔP | CAPEX | OPEX/hr
Shell & Tube Feed Pre-Cooler | TEMA R-Type Shell, Duty: 5.7 kW Thermal | 15.2 m2 Design Geometry | 12.2 m2 Exchange Surface | 650.0 kg/hr Process Gas | 0.05 bar | ₹3,13,600 | ₹4.97
Absorber Packed Column Tower | Mellapak 250Y Structured Column Configuration | 1142.2 kg/hr Hydraulic flood limit | 650.0 kg/hr gas throughput | Gas: 650.0 kg/hr ¦ Liq: 1786.9 kg/hr | 0.03 bar (6.0 mbar/m packing) | ₹4,03,200 | ₹6.11
Lean/Rich Solvent Circulation Pumps | API 610 Centrifugal Single Stage Motor Package | 12.0 GPM Pump Curve Limit | 10.1 GPM Impeller Push | 1833.6 kg/hr fluid loop | -1.50 bar (Dynamic System Head) | ₹4,92,800 | ₹7.24
TOTAL |  |  |  |  |  | ₹11,20,000 | ₹14.20
Net Recovery Efficiency: 72.8% · Total Package CAPEX: ₹11,20,000 · Total OPEX: ₹14.20/hr
Shell: Estimated recovery contribution 72.8% with Shell & Tube Feed Pre-Cooler sized for the stated duty.
Absorber: Estimated recovery contribution 72.8% with Absorber Packed Column Tower sized for the stated duty.
Lean/Rich: Estimated recovery contribution 72.8% with Lean/Rich Solvent Circulation Pumps sized for the stated duty.

## Slide 8
Technology Comparison Matrix
June 2026
HCRecov Demonstration Plant · HCRecov Engineering Team · Slide 8 / 10
Multi-Criteria Technology Comparison
Criterion | Membrane | PSA | Absorption
Net Recovery | YES | YES | YES
Lower CAPEX | NO | NO | YES
Recommended | YES | NO | NO

## Slide 9
Key Findings & Engineering Recommendation
June 2026
HCRecov Demonstration Plant · HCRecov Engineering Team · Slide 9 / 10
Key Findings
1
Membrane-based recovery offers the highest net monomer recovery at the stated feed conditions.
2
PSA remains a competitive alternative where a higher-pressure swing structure is acceptable.
3
Absorption is the most conservative option but carries the highest solvent-handling burden.
RECOMMENDATION · Advance the membrane-based option for pilot confirmation, with PSA retained as the secondary fallback path.

## Slide 10
Summary
Feed: 650 kg/hr · 1.2 bar(a) · 64 °C · 5 mol% C3H6
Membrane: 78.5% recovery | CAPEX ₹1377.8L · Below 90% minimum
PSA: 76.2% recovery | CAPEX ₹1185.7L · Below 90% minimum
Absorption: 72.8% recovery | CAPEX ₹935.2L · Below 90% minimum
No technology currently meets the 90% recovery target
Generated: undefined · HCRecov 1.0